## Slide 1: Consistency & coherency
Ehsan Yousefzadeh-Asl
E-mail: ehsanyusefzadehasl@gmail.com
February - 2021
Notes: NOTE:
To change the image on this slide, select the picture and delete it. Then click the Pictures icon in the placeholder to insert your own image.

## Slide 2: Content
Introduction
Motivation for Memory Consistency Models and Cache Coherence
Cache Coherence Basics
Memory Model and Sequential Consistency (SC)
Total Store Order (TSO), and the X86 Memory Model
Relaxed Memory Models
Memory Consistency Models and Cache Coherence for GPUs

## Slide 3: Introduction
Modern processing systems’ architects’ concern
  Ensuring the correctness
Modern Computing Systems
  Multi-Core Systems
  Heterogeneous Systems
  PIM Systems
Memory Model
  Architecturally Visible Definition of Shared Memory Correctness
  Order of accesses to Memory
  Other names: Memory Consistency, Memory Consistency Model, Consistency
Cache Coherence
  Architecturally Invisible
  A part of Memory Model
Goal: Ensuring Correctness of the programmer’s program semantics
Note: Cache Coherence as a part of Memory Model

## Slide 4: Motivation
Consider the example
Intuition: Coherence tries to make the caches of a shared-memory system invisible.

## Slide 5: Cache coherence basics

## Slide 6: Cache Coherence Basics (Part 1)
The actors in a Multi-Core system that lead to incoherence
  Processing cores
  DMA engines
  External Devices with R/W accesses to caches and memory
Idea
  Cache Coherence has to ensure that writes to each private data caches are made visible to all other processors
Cache Coherence Protocols
  Consistency-agnostic Protocols:
    Synchronous propagation of write
    An illusion of atomic memory
  Consistency-directed Protocols
    Adhering to the memory model
    Suitable for throughput-based systems: GPGPUs, Heterogeneous systems

## Slide 7: Cache Coherence Basics (Part 2)
Two invariants that must be satisfied by the cache coherence protocol
  SWMR Invariant: Single Write Multiple Read to a single location of memory
  Data-Value Invariant: The value of the memory location at the start of an epoch must be same as the value of the memory location at the end of the last read-write epoch.

## Slide 8: Memory Consistency & SC

## Slide 9: Memory Consistency (Part 1)
Memory consistency defines what programmers and implementers act based on it.
Keeping up with examples would be clearer.
But, we know Modern Processors reorder writes! So!
Question
Does the mentioned problem relate to cache coherence? How?
Answer
No! It is caused by optimizations made in a single-core execution!

## Slide 10: Memory Consistency (Part 2)
Different outcomes of a program running several times

## Slide 11: Memory Consistency (Part 3)
Fact about Modern Processors
  They are non-deterministic
Determinism is just an illusion
  Sometimes created with appropriate synchronizations by software
Wrap Up
Cache Coherence != Memory Consistency
Memory Consistency Implementation can use CC as a Black Box

## Slide 12: Sequential Consistency (SC)
The order of accesses to memory is same as specified in the program

## Slide 13: Sequential Consistency (SC) implementation
Very Naive
Less Naive

## Slide 14: Total Store Order (TSO) & X86 Memory Model

## Slide 15: Motivation
Modern Processor employ write buffers
For a single-core processor, a write buffer is invisible by ensuring that a load to an address return the value of the most recent store to that address from the buffer
  Done by bypassing
  Or by Stalling (Naive approach resulting in performance degradation)
With write buffers, hardware doesn’t respects SC
Solutions
  Turning off write buffers (vendors care about performance)
  SPARC and X86 solution: FIFO Write Buffers (TSO : Total Store Order)

## Slide 16: Formalization
SC requires program order preserving for each of the following orders
Load  Load
Load  Store
Store  Store (This constraint on TSO means that the write buffer should be a FIFO.)
Store  Load (when this constraint is omitted from TSO cores will be able to have write buffers.)
Programmers and compilers can prevent the execution of the TSO of the cases 5 and 6 in the above example by using FENCE instructions between stores and loads.

## Slide 17: Relaxed Memory Models

## Slide 19: Memory Consistency Models and Cache Coherence for GPUs